SAM Series Analog Clock

The secondary clock shall be Sapling SAM Series clock with automatic protocol detection. The clock will have plug and play features with no settings required. The clock shall have self–diagnostic capabilities for protocol detection, last received communication time and a comprehensive analysis of the entire clock. The clock will be capable of having remote diagnostic capabilities from the master clock location. The clock shall have automatic polarity detection, as well as a maximum correction time of five (5) minutes.  The clock shall be designed to be used in either a 2-wire or 3-wire system with Sapling’s SMA 2000 or 3000 Series Master Clock.  When using Sapling’s 2-wire Digital Communication, the clock will immediately self–correct upon receipt of the digital signal. The secondary clock shall also have the ability to accept sync–wire communication protocols with hourly and daily correction. The secondary clock is to have a microprocessor based movement. The clock shall have a low–profile, semi–flush smooth surface metal case. The crystal will be shatterproof polycarbonate material. Glass and visible molding marks are unacceptable. The clocks will be able to be mounted to a standard single gang box. The clock is to have black hour and minute hands, as well as a red second hand. The clock shall have UL, cUL and FCC compliance.