SAP Series Analog Clock

The secondary clock shall be Sapling SAP Series IP analog clock. The clock shall be able to receive time from up to 10 SNTP or NTP time servers.  The clock shall be able to perform diagnostics to determine when it last received communication, as well as a mechanical test of the clock itself.  The secondary clock is to have a microprocessor based movement. The clock shall have a low–profile, semi–flush smooth surface metal case. The crystal will be shatterproof polycarbonate material. Glass and visible molding marks are unacceptable. The clocks will be able to be mounted to a standard single gang box. The clock is to have black hour and minute hands, as well as a red second hand. The clock shall have UL, cUL and FCC compliance.