SMA 2000 Series Master Clock

The Master Clock shall be the Sapling SMA 2000 Series. The master clock shall have a LED display and two push switches.  The master clock shall be capable of receiving a signal from any SNTP time server via the Internet.  The master clock shall have up to ten pre-programmed SNTP servers to use in case the clock does not receive time from one of the servers via a web interface.  The master clock will be capable of receiving signals from all Sapling Master Clocks via RS485, as well as 59 minute correction, 58 minute correction, National Time and Rauland, and Dukane. The master clock shall have the capability of transferring a wired system into a wireless system. The master clock shall contain two clock circuits that have the capability to run synchronous wire systems such as 59 minute correction, 58 minute correction, National Time/Rauland or a once a day pulse for intercom systems.  The master clock shall be programmed via the two push switches on the front panel.  The master clock shall be capable of interfacing with the SAM Series analog clock via the Converter Box, and the SRM Series analog clock and SBD 1000 digital clock via RS485. The master clock shall be powered by 110VAC/60 Hz or 220VAC/50 Hz.  The master clock is pending FCC approval.

SMA 2000 upgrade options

Master clock - The master clock shall be capable of transmitting data to the SAL wireless analog clock and the SBL wireless digital clock.  The master clock shall be capable of acting as a repeater while receiving a signal wired or wirelessly from the main master clock.  The master clock shall utilize 915–928 MHz frequency–hopping technology.

GPS – The master clock shall have the option of having a GPS receiver built into the unit for synchronization from the satellites via UTC.

Web Interface – The master clock shall be able to be programmed completely from a web interface that can be accessed through any typical web browser such as Microsoft Internet Explorer or Mozilla FireFox.  The interface shall allow the user to program all display features, IP settings of the master clock and any system setting that the master clock has.

SNTP Server – The master clock shall have the capability to act as a SNTP server that other devices can point to in order to receive the time through SNTP protocol.